## Slide 1: Digital Design & Computer Arch. Lecture 6: Sequential Logic Design
Prof. Onur Mutlu
ETH Zürich
Spring 2020
6 March 2020

## Slide 2: We Are Almost Done with This
Building blocks of modern computers
  Transistors
  Logic gates
Combinational circuits
Boolean algebra
How to use Boolean algebra to represent combinational circuits
Minimizing logic circuits

## Slide 3: Agenda for Today and Next Week
Today
  Wrap up Combinational Logic and Circuit Minimization
  Start (and finish) Sequential Logic
Next week
  Hardware Description Languages and Verilog
    Combinational Logic
    Sequential Logic
  Timing and Verification

## Slide 4: Assignment: Required Lecture Video
Why study computer architecture?
Why is it important?
Future Computing Architectures
Required Assignment
  Watch Prof. Mutlu’s inaugural lecture at ETH and understand it
  https://www.youtube.com/watch?v=kgiZlSOcGFM
Optional Assignment – for 1% extra credit
  Write a 1-page summary of the lecture and email us
    What are your key takeaways?
    What did you learn?
    What did you like or dislike?
    Submit your summary to Moodle – Deadline: March 25

## Slide 5: Extra Assignment: Moore’s Law (I)
Paper review
G.E. Moore. "Cramming more components onto integrated circuits," Electronics magazine, 1965
Optional Assignment – for 1% extra credit
  Write a 1-page review
  Upload PDF file to Moodle – Deadline: April 1
I strongly recommend that you follow my guidelines for (paper) review (see next slide)

## Slide 6: Extra Assignment 2: Moore’s Law (II)
Guidelines on how to review papers critically
  Guideline slides: pdf ppt
  Video: https://www.youtube.com/watch?v=tOL6FANAJ8c
  Example reviews on “Main Memory Scaling: Challenges and Solution Directions” (link to the paper)
    Review 1
    Review 2
  Example review on “Staged memory scheduling: Achieving high performance and scalability in heterogeneous systems” (link to the paper)
    Review 1

## Slide 7: Assignment: Required Readings
Combinational Logic
  P&P Chapter 3 until 3.3 + H&H Chapter 2
Sequential Logic
  P&P Chapter 3.4 until end + H&H Chapter 3 in full
Hardware Description Languages and Verilog
  H&H Chapter 4 in full
Timing and Verification
  H&H Chapters 2.9 and 3.5 + (start Chapter 5)
By the end of next week, make sure you are done with
  P&P Chapters 1-3 + H&H Chapters 1-4

## Slide 8: Wrap-Up Combinational Logic Circuits and Design

## Slide 9: Recall: Tri-State Buffer
A tri-state buffer enables gating of different signals onto a wire
Floating signal (Z): Signal that is not driven by any circuit
  Open circuit, floating wire

## Slide 10: Recall: Example: Use of Tri-State Buffers
Imagine a wire connecting the CPU and memory
  At any time only the CPU or the memory can place a value on the wire, both not both
  You can have two tri-state buffers: one driven by CPU, the other memory; and ensure at most one is enabled at any time

## Slide 11: Recall: Example Design with Tri-State Buffers
CPU
Memory
GateMem
GateCPU
Shared Bus

## Slide 12: Recall: Another Example

## Slide 13: Multiplexer Using Tri-State Buffers

## Slide 14: Aside: Logic Using Multiplexers
Multiplexers can be used as lookup tables to perform logic functions

## Slide 15: Aside: Logic Using Multiplexers (II)
Multiplexers can be used as lookup tables to perform logic functions

## Slide 16: Aside: Logic Using Multiplexers (III)
Multiplexers can be used as lookup tables to perform logic functions
Read H&H Chapter 2.8

## Slide 17: Aside: Logic Using Decoders (I)
Decoders can be combined with OR gates to build logic functions.
Read H&H Chapter 2.8

## Slide 18: Logic Simplification using Boolean Algebra Rules

## Slide 19: Recall: Full Adder in SOP Form Logic
Full Adder

## Slide 20: Goal: Simplified Full Adder
How do we simplify Boolean logic?

## Slide 21: Quick Recap on Logic Simplification
The original Boolean expression (i.e., logic circuit) may not be optimal
Can we reduce a given Boolean expression to an equivalent expression with fewer terms?
The goal of logic simplification:
  Reduce the number of gates/inputs
  Reduce implementation cost
F = ~A(A + B) + (B + AA)(A + ~B)
F = A + B
A basis for what the automated design tools are doing today

## Slide 22: Logic Simplification
Systematic techniques for simplifications
  amenable to automation
Key Tool: The Uniting Theorem —
A's value does NOT change within the ON-set rows
B's value changes within the rows where F==1 (“ON set”)
B's value stays the same within the ON-set rows
A's value changes within the ON-set rows
➙ B is eliminated, A remains
➙ A is eliminated, B remains
If an input (B) can change without changing the output, that input value is not needed
Essence of Simplification:
Find two element subsets of the ON-set where only one variable changes its value. This single varying variable can be eliminated!

## Slide 23: Logic Simplification: Karnaugh Maps (K-Maps)

## Slide 24: Karnaugh Maps are Fun…
A pictorial way of minimizing circuits by visualizing opportunities for simplification
They are for you to study on your own…
See Backup Slides
Read H&H Section 2.7
Watch videos of Lectures 5 and 6 from 2019 Digitech course:
  https://youtu.be/0ks0PeaOUjE?list=PL5Q2soXY2Zi8J58xLKBNFQFHRO3GrXxA9&t=4570
  https://youtu.be/ozs18ARNG6s?list=PL5Q2soXY2Zi8J58xLKBNFQFHRO3GrXxA9&t=220

## Slide 25: Sequential Logic Circuits and Design

## Slide 26: What We Will Learn Today
Circuits that can store information
  Cross-coupled inverter
  R-S Latch
  Gated D Latch
  D Flip-Flop
  Register
Finite State Machines (FSM)
  Moore Machine
  Mealy Machine
Verilog implementations of sequential circuits (next week)

## Slide 27: Circuits that Can Store Information

## Slide 28: Introduction
Combinational circuit output depends only on current input
We want circuits that produce output depending on current and past input values – circuits with memory
How can we design a circuit that stores information?
Sequential Circuit
Combinational
Circuit
inputs
outputs
Storage
Element

## Slide 29: Capturing Data

## Slide 30: Basic Element: Cross-Coupled Inverters
Has two stable states: Q=1 or Q=0.
Has a third possible “metastable” state with both outputs oscillating between 0 and 1 (we will see this later)
Not useful without a control mechanism for setting Q
Image source: Harris and Harris, Digital Design and Computer Architecture, 2nd Ed., p.110.

## Slide 31: More Realistic Storage Elements
Have a control mechanism for setting Q
  We will see the R-S latch soon
  Let’s look at an SRAM (static random access memory) cell first
We will get back to SRAM (and DRAM) later
SRAM cell

## Slide 32: The Big Picture: Storage Elements
Latches and Flip-Flops
  Very fast, parallel access
  Very expensive (one bit costs tens of transistors)
Static RAM (SRAM)
  Relatively fast, only one data word at a time
  Expensive (one bit costs 6+ transistors)
Dynamic RAM (DRAM)
  Slower, one data word at a time, reading destroys content (refresh), needs special process for manufacturing
  Cheap (one bit costs only one transistor plus one capacitor)
Other storage technology (flash memory, hard disk, tape)
  Much slower, access takes a long time, non-volatile
  Very cheap

## Slide 33: Basic Storage Element: The R-S Latch

## Slide 34: The R-S (Reset-Set) Latch
Cross-coupled NAND gates
  Data is stored at Q (inverse at Q’)
  S and R are control inputs
    In quiescent (idle) state, both S and R are held at 1
    S (set): drive S to 0 (keeping R at 1) to change Q to 1
    R (reset): drive R to 0 (keeping S at 1) to change Q to 0
S and R should never both be 0 at the same time
S
R
Q’
Q
Input |  | Output
R | S | Q
1 | 1 | Qprev
1 | 0 | 1
0 | 1 | 0
0 | 0 | Forbidden

## Slide 35: Why not R=S=0?
1
0
If R=S=0, Q and Q’ will both settle to 1, which breaks our invariant that Q = !Q’
If S and R transition back to 1 at the same time, Q and Q’ begin to oscillate between 1 and 0 because their final values depend on each other (metastability)
  This eventually settles depending on variation in the circuits (more metastability to come in Lecture 8)
S
R
Q’
Q
Input |  | Output
R | S | Q
1 | 1 | Qprev
1 | 0 | 1
0 | 1 | 0
0 | 0 | Forbidden
1
0
0
0
1
1

## Slide 36: The Gated D Latch

## Slide 37: The Gated D Latch
How do we guarantee correct operation of an R-S Latch?
S
R
Q’
Q

## Slide 38: The Gated D Latch
How do we guarantee correct operation of an R-S Latch?
  Add two more NAND gates!
  Q takes the value of D, when write enable (WE) is set to 1
  S and R can never be 0 at the same time!
S
R
Q’
Q
Write
Enable
D

## Slide 39: The Gated D Latch
S
R
Q’
Q
Write
Enable
D
Input |  | Output
WE | D | Q
0 | 0 | Qprev
0 | 1 | Qprev
1 | 0 | 0
1 | 1 | 1

## Slide 40: The Register

## Slide 41: The Register
D
Q
How can we use D latches to store more data?
Use more D latches!
A single WE signal for all latches for
simultaneous writes
D2
Q2
D1
Q1
D0
Q0
3
3
Write Enable
Here we have a register, or a structure that stores more than one bit and can be read from and written to
This register holds 4 bits, and its data is referenced as Q[3:0]

## Slide 42: The Register
How can we use D latches to store more data?
Use more D latches!
A single WE signal for all latches for
simultaneous writes
Register x (Rx)
D3:0
Q3:0
WE
4
4
Here we have a register, or a structure that stores more than one bit and can be read from and written to
This register holds 4 bits, and its data is referenced as Q[3:0]

## Slide 43: Memory

## Slide 44: Memory
Memory is comprised of locations that can be written to or read from. An example memory array with 4 locations:
Every unique location in memory is indexed with a unique address. 4 locations require 2 address bits (log[#locations]).
Addressability: the number of bits of information stored in each location. This example: addressability is 8 bits.
The entire set of unique locations in memory is referred to as the address space.
Typical memory is MUCH larger (billions of locations)
Addr(00):
Addr(10):
Addr(01):
Addr(11):
0100 1001
0010 0010
0100 1011
1100 1001

## Slide 45: Addressing Memory
Let’s implement a simple memory array with:
3-bit addressability & address space size of 2 (total of 6 bits)
D
Q
WE
1 Bit
Bit2
Bit1
Bit0
Bit2
Bit1
Bit0
Addr(0)
Addr(1)
6-Bit Memory Array
Notes: Memory array

## Slide 46: Reading from Memory
How can we select the address to read?
Because there are 2 addresses, address size is log(2)=1 bit
Notes: How do we read from memory?

## Slide 47: Reading from Memory
How can we select an address to read?
Because there are 2 addresses, address size is log(2)=1 bit
D[2]
D[1]
D[0]
Addr[0]
Wordline

## Slide 48: Reading from Memory
Address Decoder
How can we select an address to read?
Because there are 2 addresses, address size is log(2)=1 bit
D[2]
D[1]
D[0]
Addr[0]
Wordline

## Slide 49: Reading from Memory
Address Decoder
How can we select an address to read?
Because there are 2 addresses, address size is log(2)=1 bit
D[2]
D[1]
D[0]
Addr[0]
Multiplexer
Wordline

## Slide 50: Writing to Memory
How can we select an address and write to it?
Notes: How can we write to memory?

## Slide 51: Writing to Memory
How can we select an address and write to it?
Input is indicated with Di
Di[2]
Di[1]
Di[0]
Addr[0]
WE

## Slide 52: Putting it all Together
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[0]
WE
Let’s enable reading and writing to a memory array
Notes: Putting it all together...

## Slide 53: A Bigger Memory Array
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[1:0]
WE
Notes: A bigger memory array

## Slide 54: A Bigger Memory Array
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[1:0]
WE
Address Decoder
Multiplexer

## Slide 55: Sequential Logic Circuits

## Slide 56: Sequential Logic Circuits
We have looked at designs of circuit elements that can store information
Now, we will use these elements to build circuits that remember past inputs
https://www.easykeys.com/228_ESP_Combination_Lock.aspx
https://www.fosmon.com/product/tsa-approved-lock-4-dial-combo
Sequential
Opens depending on past inputs
Combinational
Only depends on current inputs

## Slide 57: State
In order for this lock to work, it has to keep track (remember) of the past events!
If passcode is R13-L22-R3, sequence of states to unlock:
  The lock is not open (locked), and no relevant operations have been performed
  Locked but user has completed R13
  Locked but user has completed R13-L22
  Unlocked: user has completed R13-L22-R3
The state of a system is a snapshot of all relevant elements of the system at the moment of the snapshot
  To open the lock, states A-D must be completed in order
  If anything else happens (e.g., L5), lock returns to state A

## Slide 58: State Diagram of Our Sequential Lock
Completely describes the operation of the sequential lock
We will understand “state diagrams” fully later today
Image source: Patt and Patel, “Introduction to Computing Systems”, 2nd ed., page 76.

## Slide 59: Another Simple Example of State
A standard Swiss traffic light has 4 states
  Green
  Yellow
  Red
  Red and Yellow
The sequence of these states are always as follows
A
B
C
D

## Slide 60: Changing State: The Notion of Clock (I)
When should the light change from one state to another?
We need a clock to dictate when to change state
  Clock signal alternates between 0 & 1
At the start of a clock cycle ( ), system state changes
  During a clock cycle, the state stays constant
  In this traffic light example, we are assuming the traffic light stays in each state an equal amount of time
A
B
C
D
CLK:
0
1

## Slide 61: Changing State: The Notion of Clock (II)
Clock is a general mechanism that triggers transition from one state to another in a sequential circuit
Clock synchronizes state changes across many sequential circuit elements
Combinational logic evaluates for the length of the clock cycle
Clock cycle should be chosen to accommodate maximum combinational circuit delay
  More on this later, when we discuss timing

## Slide 62: Finite State Machines

## Slide 63: Finite State Machines
What is a Finite State Machine (FSM)?
  A discrete-time model of a stateful system
  Each state represents a snapshot of the system at a given time
An FSM pictorially shows
  1. the set of all possible states that a system can be in
  2. how the system transitions from one state to another
An FSM can model
  A traffic light, an elevator, fan speed, a microprocessor, etc.
An FSM enables us to pictorially think of a stateful system using simple diagrams

## Slide 64: Finite State Machines (FSMs) Consist of:
Five elements:
  A finite number of states
    State: snapshot of all relevant elements of the system at the time of the snapshot
  A finite number of external inputs
  A finite number of external outputs
  An explicit specification of all state transitions
    How to get from one state to another
  An explicit specification of what determines each external output value

## Slide 65: Finite State Machines (FSMs)
Each FSM consists of three separate parts:
  next state logic
  state register
  output logic
state register
At the beginning of the clock cycle, next state is latched into the state register

## Slide 66: Finite State Machines (FSMs) Consist of:
Sequential circuits
  State register(s)
    Store the current state and
    Load the next state at the clock edge
Combinational Circuits
  Next state logic
    Determines what the next state will be
  Output logic
    Generates the outputs
Notes: discuss DFlipFlop here. Latch doesn't do this, so we need sequential circuit that stores state and loads next state at the clock edge. next state is available for the full clock cycle
now lets take a look at this.

## Slide 67: Finite State Machines (FSMs) Consist of:
Sequential circuits
  State register(s)
    Store the current state and
    Load the next state at the clock edge
Combinational Circuits
  Next state logic
    Determines what the next state will be
  Output logic
    Generates the outputs
Notes: discuss DFlipFlop here. Latch doesn't do this, so we need sequential circuit that stores state and loads next state at the clock edge. next state is available for the full clock cycle
now lets take a look at this.

## Slide 68: State Register Implementation
How can we implement a state register? Two properties:
  1. We need to store data at the beginning of every clock cycle
  2. The data must be available during the entire clock cycle
CLK:
0
1
Register
Input:
Register
Output:
Desired behavior
Notes: Introduce clock much earlier maybe.
input data is sampled once.

## Slide 69: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  Whenever the clock is high, the latch propagates D to Q
  The latch is transparent
D
Q
CLK = WE
CLK:
0
1
Register
Input:
Register
Output:
Recall the
Gated D Latch

## Slide 70: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  Whenever the clock is high, the latch propagates D to Q
  The latch is transparent
D
Q
CLK = WE
CLK:
0
1
Register
Input:
Register
Output:
Recall the
Gated D Latch
Undesirable!

## Slide 71: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  When the clock is high Q will not take on D’s value AND
  When the clock is low the latch will propagate D to Q
D
Q
CLK = WE
CLK:
0
1
Input:
Output:
Recall the
Gated D Latch
How can we change the latch, so that
1) D (input) is observable at Q (output)
only at the beginning of next clock cycle?
2) Q is available for the full clock cycle

## Slide 72: The Need for a New Storage Element
To design viable FSMs
We need storage elements that allow us
  to read the current state throughout the current clock cycle
  AND
  not write the next state values into the storage elements until the beginning of the next clock cycle.

## Slide 73: The D Flip-Flop
1) state change on clock edge, 2) data available for full cycle
D Latch (Slave)
D Latch (Master)
D
Q
CLK
When the clock is low, master propagates D to the input of slave (Q unchanged)
Only when the clock is high, slave latches D (Q stores D)
  At the rising edge of clock (clock going from 0->1), Q gets assigned D
CLK:
0
1

## Slide 74: The D Flip-Flop
1) state change on clock edge, 2) data available for full cycle
At the rising edge of clock (clock going from 0->1), Q gets assigned D
At all other times, Q is unchanged
CLK:
0
1
CLK
D
Q
Q
__
D Flip-Flop

## Slide 75: The D Flip-Flop
How do we implement this?
At the rising edge of clock (clock going from 0->1), Q gets assigned D
At all other times, Q is unchanged
CLK:
0
1
CLK
D
Q
Q
__
D Flip-Flop
We can use these Flip-Flops
to implement the state register!

## Slide 76: Rising-Clock-Edge Triggered Flip-Flop
Two inputs: CLK, D
Function
  The flip-flop “samples” D on the rising edge
  of CLK (positive edge)
  When CLK rises from 0 to 1, D passes
  through to Q
  Otherwise, Q holds its previous value
  Q changes only on the rising edge of CLK
A flip-flop is called an edge-triggered state element because it captures data on the clock edge
  A latch is a level-triggered state element
CLK

## Slide 77: Register
Multiple parallel flip-flops, each of which storing 1 bit
This register stores 4 bits
This line represents 4 wires
Condensed

## Slide 78: A 4-Bit D-Flip-Flop-Based Register (Internally)
Image source: Patt and Patel, “Introduction to Computing Systems”, 3rd ed., tentative page 95.

## Slide 79: Finite State Machines (FSMs)
Next state is determined by the current state and the inputs
Two types of finite state machines differ in the output logic:
  Moore FSM: outputs depend only on the current state

## Slide 80: Finite State Machines (FSMs)
Next state is determined by the current state and the inputs
Two types of finite state machines differ in the output logic:
  Moore FSM: outputs depend only on the current state
  Mealy FSM: outputs depend on the current state and the inputs

## Slide 81: Finite State Machine Example
“Smart” traffic light controller
  2 inputs:
    Traffic sensors: TA , TB (TRUE when there’s traffic)
  2 outputs:
    Lights: LA , LB (Red, Yellow, Green)
  State can change every 5 seconds
    Except if green and traffic, stay green
From H&H Section 3.4.1

## Slide 82: Finite State Machine Black Box
Inputs: CLK, Reset, TA , TB
Outputs: LA , LB

## Slide 83: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 84: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 85: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 86: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 87: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 88: Finite State Machine: State Transition Table

## Slide 89: FSM State Transition Table
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | 
S0 | 1 | X | 
S1 | X | X | 
S2 | X | 0 | 
S2 | X | 1 | 
S3 | X | X | 

## Slide 90: FSM State Transition Table
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0

## Slide 91: FSM State Transition Table
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11

## Slide 92: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11

## Slide 93: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = ?

## Slide 94: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = (S1 ∙ S0) + (S1 ∙ S0 ∙ TB) + (S1 ∙ S0 ∙ TB)

## Slide 95: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = (S1 ∙ S0) + (S1 ∙ S0 ∙ TB) + (S1 ∙ S0 ∙ TB)
S’0 = ?

## Slide 96: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = (S1 ∙ S0) + (S1 ∙ S0 ∙ TB) + (S1 ∙ S0 ∙ TB)
S’0 = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 97: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = S1 xor S0 (Simplified)
S’0 = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 98: Finite State Machine: Output Table

## Slide 99: FSM Output Table
Current State |  | Outputs | 
S1 | S0 | LA | LB
0 | 0 | green | red
0 | 1 | yellow | red
1 | 0 | red | green
1 | 1 | red | yellow

## Slide 100: FSM Output Table
Current State |  | Outputs | 
S1 | S0 | LA | LB
0 | 0 | green | red
0 | 1 | yellow | red
1 | 0 | red | green
1 | 1 | red | yellow
Output | Encoding
green | 00
yellow | 01
red | 10
70

## Slide 101: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1

## Slide 102: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1 ∙ S0

## Slide 103: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1

## Slide 104: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1
LB0 = S1 ∙ S0

## Slide 105: Finite State Machine: Schematic

## Slide 106: FSM Schematic: State Register

## Slide 107: FSM Schematic: State Register

## Slide 108: FSM Schematic: Next State Logic
S’1 = S1 xor S0
S’0 = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 109: FSM Schematic: Output Logic
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1
LB0 = S1 ∙ S0

## Slide 110: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 111: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 112: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 113: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 114: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 115: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 116: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 117: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB
This is from H&H Section 3.4.1

## Slide 118: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 119: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB
See H&H Chapter 3.4

## Slide 120: Finite State Machine: State Encoding

## Slide 121: FSM State Encoding
How do we encode the state bits?
  Three common state binary encodings with different tradeoffs
    Fully Encoded
    1-Hot Encoded
    Output Encoded
Let’s see an example Swiss traffic light with 4 states
  Green, Yellow, Red, Yellow+Red

## Slide 122: FSM State Encoding (II)
Binary Encoding (Full Encoding):
  Use the minimum number of bits used to encode all states
    Use log2(num_states) bits to represent the states
  Example states: 00, 01, 10, 11
  Minimizes # flip-flops, but not necessarily output logic or next state logic
One-Hot Encoding:
  Each bit encodes a different state
    Uses num_states bits to represent the states
    Exactly 1 bit is “hot” for a given state
  Example states: 0001, 0010, 0100, 1000
  Simplest design process – very automatable
  Maximizes # flip-flops, minimizes next state logic

## Slide 123: FSM State Encoding (III)
Output Encoding:
  Outputs are directly accessible in the state encoding
  For example, since we have 3 outputs (light color), encode state with 3 bits, where each bit represents a color
  Example states: 001, 010, 100, 110
    Bit0 encodes green light output,
    Bit1 encodes yellow light output
    Bit2 encodes red light output
  Minimizes output logic
  Only works for Moore Machines (output function of state)

## Slide 124: FSM State Encoding (III)
Output Encoding:
  Outputs are directly accessible in the state encoding
  For example, since we have 3 outputs (light color), encode state with 3 bits, where each bit represents a color
  Example states: 001, 010, 100, 110
    Bit0 encodes green light output,
    Bit1 encodes yellow light output
    Bit2 encodes red light output
  Minimizes output logic
  Only works for Moore Machines (output function of state)
The designer must carefully choose
an encoding scheme to optimize the design under given constraints

## Slide 125: Moore vs. Mealy Machines

## Slide 126: Recall: Moore vs. Mealy FSMs
Next state is determined by the current state and the inputs
Two types of finite state machines differ in the output logic:
  Moore FSM: outputs depend only on the current state
  Mealy FSM: outputs depend on the current state and the inputs

## Slide 127: Moore vs. Mealy FSM Examples
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it.
The snail smiles whenever the last four digits it has crawled over are 1101.
Design Moore and Mealy FSMs of the snail’s brain.

## Slide 128: Moore vs. Mealy FSM Examples
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it.
The snail smiles whenever the last four digits it has crawled over are 1101.
Design Moore and Mealy FSMs of the snail’s brain.

## Slide 129: State Transition Diagrams
What are the tradeoffs?

## Slide 130: FSM Design Procedure
Determine all possible states of your machine
Develop a state transition diagram
  Generally this is done from a textual description
  You need to 1) determine the inputs and outputs for each state and 2) figure out how to get from one state to another
Approach
  Start by defining the reset state and what happens from it – this is typically an easy point to start from
  Then continue to add transitions and states
  Picking good state names is very important
  Building an FSM is like programming (but it is not programming!)
    An FSM has a sequential “control-flow” like a program with conditionals and goto’s
    The if-then-else construct is controlled by one or more inputs
    The outputs are controlled by the state or the inputs
  In hardware, we typically have many concurrent FSMs

## Slide 131: What is to Come: LC-3 Processor

## Slide 132: What is to Come: LC-3 Datapath

## Slide 133: Digital Design & Computer Arch. Lecture 6: Sequential Logic Design
Prof. Onur Mutlu
ETH Zürich
Spring 2020
6 March 2020

## Slide 134: Backup Slides: Different Types of Flip Flops

## Slide 135: Enabled Flip-Flops
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function:
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state

## Slide 136: Resettable Flip-Flop
Inputs: CLK, D, Reset
  The Reset is used to set the output to 0.
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: the flip-flop behaves like an ordinary D flip-flop

## Slide 137: Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop (see Exercise 3.10)
Synchronously resettable flip-flop?

## Slide 138: Settable Flip-Flop
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves like an ordinary D flip-flop

## Slide 139: Logic Simplification: Karnaugh Maps (K-Maps)

## Slide 140: Logic Simplification
Systematic techniques for simplifications
  amenable to automation
Key Tool: The Uniting Theorem —
A's value does NOT change within the ON-set rows
B's value changes within the rows where F==1 (“ON set”)
B's value stays the same within the ON-set rows
A's value changes within the ON-set rows
➙ B is eliminated, A remains
➙ A is eliminated, B remains
If an input (B) can change without changing the output, that input value is not needed
Essence of Simplification:
Find two element subsets of the ON-set where only one variable changes its value. This single varying variable can be eliminated!

## Slide 141: Complex Cases
One example
Problem
  Easy to see how to apply Uniting Theorem…
  Hard to know if you applied it in all the right places…
  …especially in a function of many more variables
Question
  Is there an easier way to find potential simplifications?
  i.e., potential applications of Uniting Theorem…?
Answer
  Need an intrinsically geometric representation for Boolean f( )
  Something we can draw, see…

## Slide 142: Karnaugh Map
Karnaugh Map (K-map) method
  K-map is an alternative method of representing the truth table that helps visualize adjacencies in up to 6 dimensions
  Physical adjacency ↔ Logical adjacency
2-variable K-map
 |  | 0 | 1
0 |  | 00 | 01
1 |  | 10 | 11
Numbering Scheme: 00, 01, 11, 10 is called a
“Gray Code” — only a single bit (variable) changes
from one code word and the next code word
 |  | 00 | 01 | 11 | 10
00 |  | 0000 | 0001 | 0011 | 0010
01 |  | 0100 | 0101 | 0111 | 0110
11 |  | 1100 | 1101 | 1111 | 1110
10 |  | 1000 | 1001 | 1011 | 1010
3-variable K-map
4-variable K-map
 |  | 00 | 01 | 11 | 10
0 |  | 000 | 001 | 011 | 010
1 |  | 100 | 101 | 111 | 110

## Slide 143: Karnaugh Map Methods
Adjacent
000
001
010
011
110
111
100
101
000
001
010
011
110
111
100
101
Adjacent
K-map adjacencies go “around the edges”
Wrap around from first to last column
Wrap around from top row to bottom row
 |  | 00 | 01 | 11 | 10
0 |  | 000 | 001 | 011 | 010
1 |  | 100 | 101 | 111 | 110

## Slide 144: K-map Cover - 4 Input Variables
 |  | 00 | 01 | 11 | 10
00 |  | 1 | 0 | 0 | 1
01 |  | 0 | 1 | 0 | 0
11 |  | 1 | 1 | 1 | 1
10 |  | 1 | 1 | 1 | 1
Strategy for “circling” rectangles on Kmap:
As big as possible
Biggest “oops!” that people forget:
Wrap-arounds

## Slide 145: Example: As Logic Gates
What does this solution look like as gates?

## Slide 146: Logic Minimization Using K-Maps
Very simple guideline:
  Circle all the rectangular blocks of 1’s in the map, using the fewest possible number of circles
    Each circle should be as large as possible
  Read off the implicants that were circled
More formally:
  A Boolean equation is minimized when it is written as a sum of the fewest number of prime implicants
  Each circle on the K-map represents an implicant
  The largest possible circles are prime implicants

## Slide 147: K-map Rules
What can be legally combined (circled) in the K-map?
  Rectangular groups of size 2k for any integer k
  Each cell has the same value (1, for now)
  All values must be adjacent
    Wrap-around edge is okay
How does a group become a term in an expression?
  Determine which literals are constant, and which vary across group
  Eliminate varying literals, then AND the constant literals
    constant 1 ➙ use , constant 0 ➙ use
What is a good solution?
  Biggest groupings ➙ eliminate more variables (literals) in each term
  Fewest groupings ➙ fewer terms (gates) all together
  OR together all AND terms you create from individual groups

## Slide 148: K-map Example: Two-bit Comparator
Design Approach:
Write a 4-Variable K-map
for each of the 3
output functions
A | B | C | D | F1 | F2 | F3
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0
 | A |  | 
 |  | F1 | AB = CD
 | B |  | 
 |  | F2 | AB < CD
 | C |  | 
 |  | F3 | AB > CD
 | D |  | 

## Slide 149: K-map Example: Two-bit Comparator (2)
A | B | C | D | F1 | F2 | F3
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0
 |  | 00 | 01 | 11 | 10
00 |  | 1 |  |  | 
01 |  |  | 1 |  | 
11 |  |  |  | 1 | 
10 |  |  |  |  | 1
K-map for F1
F1 =
A'B'C'D' + A'BC'D + ABCD + AB'CD'

## Slide 150: K-map Example: Two-bit Comparator (3)
A | B | C | D | F1 | F2 | F3
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0
 |  | 00 | 01 | 11 | 10
00 |  |  | 1 | 1 | 1
01 |  |  |  | 1 | 1
11 |  |  |  |  | 
10 |  |  |  | 1 | 
K-map for F2
F2 =
A'C + A'B'D + B'CD
F3 =
? (Exercise for you)

## Slide 151: K-maps with “Don’t Care”
Don’t Care really means I don’t care what my circuit outputs if this appears as input
  You have an engineering choice to use DON’T CARE patterns intelligently as 1 or 0 to better simplify the circuit
I can pick 00, 01, 10, 11
independently of below
I can pick 00, 01, 10, 11
independently of above
A | B | C | D | F | G
• • • |  |  |  |  | 
0 | 1 | 1 | 0 | X | X
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 | X | X
1 | 0 | 0 | 1 |  | 
• • • |  |  |  |  | 

## Slide 152: Example: BCD Increment Function
A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | X | X | X | X
1 | 0 | 1 | 1 | X | X | X | X
1 | 1 | 0 | 0 | X | X | X | X
1 | 1 | 0 | 1 | X | X | X | X
1 | 1 | 1 | 0 | X | X | X | X
1 | 1 | 1 | 1 | X | X | X | X
BCD (Binary Coded Decimal) digits
  Encode decimal digits 0 - 9 with bit patterns 00002 — 10012
  When incremented, the decimal sequence is 0, 1, …, 8, 9, 0, 1
These input patterns should
never be encountered in practice
(hey -- it’s a BCD number!)
So, associated output values are
“Don’t Cares”

## Slide 153: K-map for BCD Increment Function
 |  | 00 | 01 | 11 | 10
00 |  | 1 |  |  | 1
01 |  | 1 |  |  | 1
11 |  | X | X | X | X
10 |  | 1 |  | X | X
A B C D
+ 1
W X Y Z
 |  | 00 | 01 | 11 | 10
00 |  |  |  |  | 
01 |  |  |  | 1 | 
11 |  | X | X | X | X
10 |  | 1 |  | X | X
 |  | 00 | 01 | 11 | 10
00 |  |  |  | 1 | 
01 |  | 1 | 1 |  | 1
11 |  | X | X | X | X
10 |  |  |  | X | X
 |  | 00 | 01 | 11 | 10
00 |  |  | 1 |  | 1
01 |  |  | 1 |  | 1
11 |  | X | X | X | X
10 |  |  |  | X | X
W
X
Z
Y
Z (without don’t cares) = A'D' + B'C'D’
Z (with don’t cares) = D'

## Slide 154: K-map Summary
Karnaugh maps as a formal systematic approach for logic simplification
2-, 3-, 4-variable K-maps
K-maps with “Don’t Care” outputs
H&H Section 2.7